# ACCELERATOR DIVISION DEPARTMENTAL PROCEDURE

# ACCELERATION OPERATIONS DEPARTMENT

# ADDP-OP-0005

Beam-on Accident in Accelerator Enclosures

MCR Emergency Response Procedure

PREPARED BY 		DATE

Walter Kissel

# AD Operations Department

APPROVED BY 		DATE

# Todd Sullivan

AD Operations Department Head

REVISION NO.    1.0    REVISION ISSUE DATE                          _

# REVIEW AND CONCURRENCE RECORD

REVIEWED BY ________________________________DATE______________

Todd Sullivan

AD Operations Department Head

REVIEWED BY ________________________________DATE______________

Any other necessary reviewer

Title goes here

| Author | Description of Change | Revision Date |
| --- | --- | --- |
| Walter Kissel | Updated required procedure format. Added flow chart. | 3/25/21 |

1.0	PURPOSE AND SCOPE	1

2.0	INSTRUCTIONS	1

3.0	DISTRIBUTION......................................................................................................2

4.0 	ATTACHMENT...............................................................................................1 of 1

# 1.0	PURPOSE AND SCOPE

The purpose of this Accelerator Division Departmental Procedure (ADDP) is to establish and define Fermilab Accelerator Division Operations Department Main Control Room (MCR) response to a Beam-On Emergency in accelerator enclosures.

2.0	RESPONSIBILITIES

2.1	Crew chief or designee shall initiate response by following included instructions.

3.0 	INSTRUCTIONS

3.1	Incoming report of person possibly exposed to beam

3.1.1	Crew Chief or designee shall turn off the Master Beam Switch and remove the following keys:

- HEP key

- NTF key

- FAST key

3.1.2 	If person is still in enclosure, turn enclosure keys for that enclosure to deenergize ESS and turn off supplies as quickly as possible.

Do Not alter machine configuration except as necessary to safely egress            exposed person from tunnel.

3.1.3 	       Get Person’s name. Encourage person to leave enclosure by most direct route

3.1.4	      Notify x3131 of possible beam on exposure.

3.1.5	Dispatch two people to assist exposed person until FFD arrives.

3.1.6	Initiate D1 save.

Copy and print all windows on all displays on all consoles in the MCR

Print D106 MISC <16,17,18,19,20>

Document machine conditions in MCR Elog.

3.1.7	Insure the following people have been informed: RSO,  DSO,  Division Head,  Department Head,  Machine Coordinator

Note: A flow chart listing the steps of this procedure are attached to this procedure.

4.0	DISTRIBUTION

Add link here

# Text boxes

Incoming report of person possibly exposed to beam

Insure the following people have been informed:

RSO,  DSO,  Division Head,  Department Head,  Machine Coordinator

Initiate D1 save.

Copy and print all windows on all displays on all consoles in the MCR

Print D106 MISC <16,17,18,19,20>

Document machine conditions.

Dispatch two people to assist exposed person until FFD arrives

Get Person’s name

Encourage person to leave enclosure by most direct route

Remove HEP key

NTF key

FAST key

Take master switch

If person is still in enclosure, turn enclosure keys for that enclosure to deenergize ESS and turn off supplies as quickly as possible.

Do Not alter machine configuration except as necessary to safely egress exposed person from tunnel.