# ACCELERATOR DIVISION DEPARTMENTAL PROCEDURE

# ACCELERATION OPERATIONS DEPARTMENT

# ADDP-OP-0007

Footprint Area Fire

MCR Emergency Response

PREPARED BY 		DATE

Walter Kissel

# AD Operations Department

APPROVED BY 		DATE

# Todd Sullivan

AD Operations Department Head

REVISION NO.    1.0    REVISION ISSUE DATE                          _

# REVIEW AND CONCURRENCE RECORD

REVIEWED BY ________________________________DATE______________

Todd Sullivan

AD Operations Department Head

REVIEWED BY ________________________________DATE______________

Any other necessary reviewer

Title goes here

| Author | Description of Change | Revision Date |
| --- | --- | --- |
| Walter Kissel | Updated required procedure format. Added flow chart. | 3/25/21 |

1.0	PURPOSE AND SCOPE	1

2.0	INSTRUCTIONS	1

3.0	DISTRIBUTION......................................................................................................1

4.0 	ATTACHMENT...............................................................................................1 of 1

# 1.0	PURPOSE AND SCOPE

The purpose of this Accelerator Division Departmental Procedure (ADDP) is to establish and define Fermilab Accelerator Division Operations Department Main Control Room (MCR) response to a report of fire in the accelerator footprint area. (MCR and surround including X-Gallery, Linac Gallery, Booster Galleries & Transfer Gallery)

2.0	RESPONSIBILITIES

2.1	Crew chief or designee shall initiate response by following included instructions.

3.0 	INSTRUCTIONS

3.1	Fire in the Footprint area

3.1.1	During an active fire alarm or a report of fire/smoke, the Crew Chief or designee shall ensure that emergency dispatch has been notified by calling x3131.

3.1.2	If the alarm is not in the Cross Gallery, the Crew Chief or designee shall turn off equipment in the area via the control system.

3.1.3	If the alarm is in the Cross Gallery, the Crew Chief or designee shall remove and maintain control of the following keys:

- HEP key

- NTF key

- FAST key

The Crew Chief or designee and on shift Operators, shall evacuate to the    parking lot.

Note: A flow chart listing the steps of this procedure are attached to this procedure.

4.0	DISTRIBUTION

Add link here

# Text boxes

Footprint Area Fire Emergency Response

Fire alarm active or report of fire/smoke in Footprint area

Ensure x3131 has been notified

Is alarm for Cross Gallery?

Evacuate to parking lot.

Remove and maintain control of

HEP key

NTF key

FAST key

Turn off equipment in area

via control system

Yes

No